Development and Demonstration of a Non-Volatile 4Mbit Chalcogenide Random Access Memory

J. Maimon

Ovonyx

8665 Sudley Rd., #263

Manassas, VA 20110

S. Ramaswamy, B. Li,

# J. Rodgers, L. Burcin

BAE SYSTEMS

9300 Wellington Rd.

Manassas, VA 20110

# K. Hunt

AFRL/VSSE

3550 Aberdeen Ave SE

Kirtland AFB, NM 87117

# Abstract

During the first stage of a multi-year research program, BAE SYSTEMS and Ovonyx have designed, fabricated and tested test chips to demonstrate full integration of a chalcogenide-based non-volatile memory element into a radiation hardened CMOS process. The test structures range from simple two- and four-point-probe material characterization macros, such as sheet resistance monitors and chalcogenide memory elements, to fully wired 64kbit memory arrays.  Process integration has progressed from the previously demonstrated stand-alone chalcogenide memory elements through full memory array fabrication.  Results of successful integration of the chalcogenide material used for phase-change applications in re-writable optical storage (Ge2Sb2Te5) with BAE SYSTEM’S 0.5µm radiation hardened CMOS to produce 64kbit arrays have been reported in the past.

In this paper we present a description of the architecture and design of a 4Mbit chalcogenide non-volatile memory for a 0.25µm radiation hardened CMOS process.  Fabrication of the design is expected to be completed by the end of 2004.  In addition, results from the C-RAM process transition (from BAE SYSTEMS’ 0.5µm to the radiation hardened 0.25µm process) will be presented.

# Introduction

Phase change nonvolatile memories are emerging as viable candidates for the next generation of solid state memory products.  Most commercial research is focused on the chalcogenide material (Ge2Sb2Te5) used for rewritable optical media (CD-RW and DVD-RW).  This alloy is the product of a long material development effort, starting in 1968.  Following initial investigations into its suitability for solid-state applications as well as optical products, improvements in device modeling provided increased optimism that memory devices could be economically produced that might rival or even surpass existing solid-state memory – both nonvolatile and volatile.

The Air Force Research Laboratory initiated a program in 1999 to research and develop chalcogenide technology for space applications.  The Chalcogenide-based Random Access Memory (C-RAM) program combines the phase-change expertise of Ovonyx, Inc. with the radiation hardened CMOS processing capability of BAE SYSTEMS to focus on a radiation-hardened, fast, low-power, high-endurance nonvolatile memory.

Today the state of the art for space non-volatile memory is a radiation tolerant 256kbit SONOS device requiring milliseconds to write (erase) and that can be written to a few thousand times.  System designers requiring a more dense, low-power, fast-access, radiation-hardened, non-volatile memory have been forced to work around these shortcomings using a variety of techniques, including commercial devices repackaged for use in space or volatile memory backed by batteries.  The first generation of C-RAM memory is designed to greatly exceed the existing solutions (in density, write speed, endurance) and close the gap that exists between requirements and availability.  Based on the success of the 64kbit C-RAM test chip, the Air Force Research Laboratory has recently funded BAE SYSTEMS to design, fabricate and deliver a 4Mbit C-RAM product. A 4Mbit C-RAM device based on the results from the 64kbit will be implemented in 0.25µm radiation-hardened CMOS.  The program will result in prototype devices 4Q04 and flight parts 3Q05. This paper will describe the 4Mbit architecture, design, and verification methodology used for the release of the product for fabrication.

References

- S.Ovshinsky, “Reversible Electrical Switching Phenomena in Disordered Structures,” Phys. Rev. Lett, V. 21, no. 20, pp. 1450-1453, Nov. 11, 1968.

- S.Ovshinsky, “Amorphous Materials- The Key to New Devices" IEEE  Proc. of CAS, v1, pp33, 1998.

- J. Maimon, E. Spall, R. Quinn, S. Schnur, “Chalcogenide-Based Non-Volatile Memory Technology”, IEEE Aerospace 2001, January 2001.

- S. Bernacki, K. Hunt, S. Tyson, S. Hudgens, B. Pashmokov, W. Czubatzj, “Total Dose Radiation Response and High Temperature Imprint Characteristics of Chalcogenide Based RAM Resistor Elements”, IEEE Trans. Nuc. Sci, v47, #6, pp2528-2533, 2000.

- J. Maimon, K. Hunt, J. Rodgers, L. Burcin, K. Knowles, “Circuit Demonstration of Radiation Hardened Chalcogenide Non-Volatile Memory”, IEEE Aerospace 2003, January 2003.

- J. Maimon, K. Hunt, J. Rodgers, L. Burcin, “Results of Radiation Effects on a Chalcogenide Non-Volatile Memory Array”, IEEE Aerospace 2004, March 2004.